An MPEG-4 SNHC Compatible Implementation of

a 3D Facial Animation System

Gabriel Antunes Abrantes, Fernando Pereira

Instituto Superior Técnico - Instituto de Telecomunicações

Av. Rovisco Pais, 1096 Lisboa Codex, PORTUGAL

Tel: + 351.1.8418460;  Fax: + 351.1.8418472

E-mail: Gabriel.Abrantes@lx.it.pt; Fernando.Pereira@lx.it.pt

Abstract

In this paper, an implementation of a 3D facial animation system, according to the MPEG-4 SNHC VM specification is presented. The system includes a 3D model of a complete human head, its animation, and an analysis methodology to extract facial features. Results are shown demonstrating the capabilities of the current implementation.

1. Background: The MPEG-4 SNHC Framework

It is nowadays more and more recognized that audiovisual content should be created and represented in a representation framework that is able to give the user as many real-world like capabilities as possible. The more it is known about the content, the more its representation can be efficient and powerful, in terms of the things one can do with it. Recognising this fact, MPEG-4 will be the first audiovisual representation standard that understands a scene as a composition of audiovisual objects with a certain spatial and temporal behaviour. In this way, MPEG-4 will be the first audiovisual standard allowing the user to interact with the scene content, the coding methodologies to depend on the content, and sending just the right content when scarce resources are available 1.

In the context of this content-based coding approach, there are no more reasons to differentiate between natural and synthetic content. According to the MPEG-4 project description 2, “The MPEG-4 project aims to establish a universal, efficient coding of different forms of audiovisual data, called audiovisual objects. These objects can be of natural and synthetic origin.” This means more precisely that MPEG-4 shall support efficient methods for combining synthetic and natural objects, the ability to code and manipulate natural and synthetic audio and video data, and decoder-controllable methods for compositing synthetic data with ordinary video and audio, allowing for interactivity. Examples of this integration of the natural and synthetic worlds are: animation and synthetic sound can be composited with natural audio and video in a game or in a broadcasting transmission; facial animations may provide more friendly user interfaces; a viewer can translate or remove a graphic overlay to view the video beneath it; graphics and sound can be ‘rendered’ from different points of observation.

In July 1996, the MPEG SNHC (Synthetic and Natural Hybrid Coding) group decided to use a bottom-up approach for its work, focusing in the first phase on particular applications as a basis for gradual extensions, leading to a framework that will be able to cover a broad range of applications. These applications ultimately involve interactions with audio, video and 3D objects, as well as human representations within 3D environments. In October 1996, and after evaluating the proposals submitted as answer to the Call for Proposals issued a few months before for technology on synthetic and natural hybrid coding, the SNHC group defined its first Verification Model (VM). A VM is a “completely defined encoding and decoding environment, composed of tools and algorithms, such that an experiment performed by multiple independent parties will produce essentially identical results”. After its first version, the SNHC VM has been updated at the following meetings 3, and it is now focusing on the following areas of work: description of synthetic human face and body, and its animation, texture coding, static and dynamic mesh coding with texture mapping, media integration of text and graphics (2D overlayed and animated text and graphics), text to speech synthesis (TTS), and its possible interface to facial animation, and description of synthetically generated audio. These areas of work should allow the SNHC group to focus their activities, in order to gather new experts interested in this natural/synthetic integration approach. More ambitious goals, such as shared virtual environments, can be later addressed, after a solid basis has been set-up for the first simpler cases.

One of the most interesting components of the SNHC VM is 3D facial animation. 3D model based coding applied to human heads may be very useful, notably for low bitrate conditions. The standardization of this technology in the essential parts to guarantee interoperability may significantly accelerate the deployment of applications using synthetic human heads. Relevant applications are the virtual talker, inter-personal communication advanced systems, games, story telling, language teaching, speech rehabilitation, tele-shopping, tele-learning, etc.

This paper intends to describe the work developed at Instituto Superior Técnico (IST) towards the implementation of an MPEG-4 SNHC compatible 3D facial animation system. More precisely, the definition of the 3D facial model (complete head), and its animation according to the SNHC VM description 3 will be described in section 2, while section 3 will present a facial analysis methodology to extract the most relevant (and MPEG-4 compatible) Facial Animation Parameters (FAPs) and Facial Definition Parameters (FDPs).

2. Implementing an SNHC Compatible 3D Facial Animation System

2.1 The 3D Facial Model

The IST 3D facial model for the complete human head is a (very) modified version of a well-known model developed by Frederic Parke 4. This model was used only as a starting point, since it only includes the front part of the head (the face), missing important parts, such as the back of the head, the tongue and the ears. As these parts are important for some expressions and animations, it was decided to improve the Parke model, leading to an IST model including the back of the head, tongue, ears and some cheeks improvements in order to obtain more realistic animations. The IST model was used in the MPEG-4 SNHC compatible 3D facial animation system here described (see figure 1).

The IST facial model is described by 1038 points and 1698 polygons, 230 points and 510 polygons of which correspond to the new parts of the head that were added to the Parke model. The model can be divided in different regions, according to their texture. The most important regions are the hair, eyebrows, mouth, teeth, tongue, eyes, nose and ears.

Figure 1 - IST Head Model (only polygons and with texture)

2.2 Animating the 3D Facial Model

The animation of the face is being made according to the SNHC VM description, using the 68 FAPs there defined. The FAPs represent a very significant set of facial actions enabling the representation of facial expressions. It is important to highlight that MPEG-4 will (only) standardize the FAPs but not the head model since this is not strictly required for interoperability. In this context, it is highly convenient to test the decoding of FAP bitstreams using different head models in order the model independence assumption is confirmed. The FDP parameter set will be used to adapt the face model to a particular face, and it is expected to be sent just once per session.

Two high-level FAPs were defined for expressions and visemes, which are not yet fully described in the SNHC VM [3], but should be easily implemented since they are based on the rest of the FAP set. So far 66 FAPs have been implemented in the IST 3D facial animation system. Each FAP updates a set of 3D points corresponding to a certain key feature of the face.

The neutral face is described in a VRML file, which contains the list of points, polygons and possible texture. For each FAP set corresponding to a frame, a new VRML file is generated in which the points describing the 3D model are changed according to the received FAPs. The FAPs are read from a file, including the number of frames, the FAP masking and the FAPs for each frame. For the moment, ‘hand made’ FAP files and some FAP files generated by the analysis of a real face are used.

3. Facial Analysis

The animation of the 3D facial model requires FAP files, which may be synthetically generated or created by the analysis of real faces, depending on the relevant application. Analysis is usually a complex task which precise constraints strongly depend on the application conditions. As a consequence, analysis may be real-time or off-line, fully automatic or human guided. While videotelephony-like applications basically require real-time and fully automatic facial analysis, storyteller applications may allow off-line, human guided analysis. Other applications such as tele-shopping, and gaming, may even not need any analysis at all since there may be no intention to reproduce a real face but just to create a realistic face.

In order to obtain a more complete system, a facial analysis block has been developed in the context of the work here described. This block will allow the use of the animation system in applications where the realistic and faithful reproduction of a talking person is important, such as for videotelephone like applications. The analysis has the objective to generate the FAP as well as the FDP set. The FDP set includes 3D feature points, which are used to locate the facial features on the 3D mesh [3], and on the texture image. The extraction of these feature points will allow texture mapping and the adaptation of the 3D model to a particular face.

Since not all FAPs and FDPs have the same relevance, the analysis approach followed here is to extract the more important FAPs and FDPs, notably those corresponding to the lips, eyes, chin and head rotation, which should be sufficient to obtain a simple but realistic animation and definition of the 3D facial model. This bottom-up approach builds up a solid basis, which will allow the progressive adding of the rest of the FAP and FDP set, according to their relevance in terms of animation and facial expression.

The implemented facial analysis considers two parts: i) detection of the head; ii) detection of the facial features (starting with mouth, chin and eyes), using the knowledge about the head position.

3.1 Head Detection

To locate the head, a snake (or active contour model) [5], which is an energy minimizing spline that is pulled towards edges, is applied to an image containing a face. In order to detect the more important edges in a picture, notably those concerning the face, the Sobel’s edge detection method is used on the original image. The snake is applied to the resulting contour image. The final position of the snake should give the location of the head. Problems appear when a background with objects that can originate high contrast edges in the contour image is present, making the snake stop in the wrong place. Problems also occur when the person has long hair on the sides of the face, leading to wrong face detection. The head position detected is used to ease the location of the eyes, mouth and chin.

3.2 Mouth and Chin Detection

For the mouth detection, a priori knowledge obtained from a test set of pictures with faces is used. From this set, it is known that in most cases the mouth area is of high contrast, located in the lower half of the face, and it is, in general, the reddest area in the face. Based on these assumptions, the mouth search area, and two images to be processed for mouth detection, will be achieved. The first image is obtained by applying vertical and horizontal gains to the contour image, depending on the corresponding probability of mouth presence. The other image is achieved using a ´red-detection process´, in which the reddest regions of the face are highlighted. This process uses the R, G and B components, and it computes the parameter R – Max (G, B), for each pixel of the image. The two images are then combined in an auxiliary image where the mouth region has the highest contrast. In this image the line that surrounds the mouth is obtained, allowing to extract some of the feature points corresponding to the mouth. Problems with this process may appear when the head detection is not so good or the face is very badly illuminated, such that there is neither a high contrast nor a redder region in the mouth area.

With the mouth location knowledge, the position of the chin is obtained. Again, from the test data set, it is known that the chin is beneath the mouth, and it usually creates a significant edge in the contour image.

3.3 Eyes Detection

For the detection of the eyes, a similar process to the mouth detection is used. From the test set, it is known the typical relative eyes position. The previously obtained mouth location is also used. Then vertical and horizontal gains, that have their peak gain at the position where the eyes most probably are, are applied to the contour image. With the auxiliary image obtained, the left and right eyes are separately searched. The search consists in looking for the strongest edge in each half of the specific face region, and from this edge the eye contours are found.

Problems may appear when the mouth is wrongly detected or when the eyebrows have such a high edge in the contour image, that they are taken for the eyes.

3.4 Model Adaptation

After obtaining the location of the head, mouth eyes, chin and the corresponding FDP feature points, it is possible to adapt the (neutral) 3D facial model to the (real) face. As mentioned before, and in spite of having sometimes bad head detection (due to background objects or long hair), the mouth, chin and the eyes are most of the times well detected. In order to reach better model adaptation and FDP feature points, the face contour is searched again using the location of the detected facial features. The FDPs allow not only to adapt the model to the face but also to map texture increasing the realism of the synthetic image.

4. Results

This section shows some results obtained with the analysis and facial animation systems here described.

4.1 Animation of the Model

Figures 2 and 3 show the animation corresponding to lips, eyelids and eyebrows FAPs, creating angry and surprised expressions.

Fig.2 – Angry face	 Fig.3 – Surprised face

4.2 Facial Analysis

The following images show how the analysis process is progressively applied to an image with a face.

Fig. 4 - Original image	Fig. 5 – Contour image

Fig. 6, 7 –  Mouth and eyes detection images

Fig. 8 – Facial features	Fig. 9 – Model adaptation

5. Final Remarks

This paper intends to describe an MPEG-4 SNHC compatible implementation of a 3D facial animation system, including a new facial model, its animation, and the automatic analysis of a face, to extract the relevant facial features. The work presented will continue with the implementation of the two high level FAPs, and the improvement of the facial analysis system, notably in terms of robustness.

6. References

[1] R. Koenen, F. Pereira, L. Chiariglione, “MPEG-4: Context and Objectives”, Image Communication Journal, vol. 9, nº 4, May 1997

[2] L. Chiariglione (Convenor), ”MPEG-4 project description”, Document ISO/IEC JTC1/SC29/WG11 N1177, Munich MPEG meeting, January 1996

3 MPEG SNHC Group, “SNHC verification model 4.0”, Document ISO/IEC JTC1/SC29/WG11 N1666, Bristol MPEG meeting, April 1997

4 Frederic I. Parke, “Parametrized Models for Facial Animation”, IEEE Computer Graphics & Applications, vol.2, nº 9, November 1982

5 M. Kass, A. Witkin, D. Terzopoulos, “Snakes: Active Contour Models”, International Journal of Computer Vision, vol. 1, nº 4, 1987